Exercises Synthesis

1	It is proposed to manufacture a chemical C with a process I that uses

raw material B.  B can either be purchased or manufactured with either

of two processes, II or III, which use chemical A as a raw material.

In order to decide the optimal selection of processes and levels of

production that maximize profit formulate the MINLP problem and solve

with the augmented penalty/outer-approximation/equality-relaxation

algorithm in DICOPT++.

Data:

Conversion:	Process     I	C = 0.9B

Process    II	B =   ln(1 + A)   Maximum capacity:   5 ton prod/hr

Process   III	B =   1.2  ln (1 + A)

(A, B, C, in ton/hr)

Prices:	A $ 1,800/ton

B $ 7,000/ton

C $13,000/ton  (maximum demand:   1 ton/hr)

Investment cost

Fixed (103$/hr)		Variable (103$/ton product)

Process      I			3.5					 2

Process     II			 1					 1

Process    III			1.5					1.2

Note:	Minimize negative of profit.

2.  Given are 3 candidate reactors for the reaction A -> B, where one would like to produce 10 kgmol/hr of B.  Up to 15 kgmol/hr of reactant A are available at a price of $2/kgmol.  The data on the three reactors is as follows:

Conversion	Linear costs	Fixed-charge cost

Reactor I		0.8		2.2feed	8.0 + 1.5feed

Reactor II		0.667		1.5feed	5.4 + 1.0feed

Reactor III		0.555		0.73feed	2.7 + 0.5feed

a)  Develop a network representation for this problem.

b)  Determine an LP formulation for linear reactor costs and solve.

c)  Determine an MILP formulation using the fixed-charge cost models and solve.

d)  Compare the solutions in b) and c) and explain qualitatively why differences exist in the 	two solutions.

3. Given is a process that involves the following hot and cold streams:

Stream		Fcp(KW/K)		Tin(K)	Tout(K)

H1			20			700		420

H2			40			620		330

H3			70			480		330

H4			94			380		330

C1			50			300		650

C2			720			375		400

The following utilities are available for satisfying heating and cooling requirements:

Fuel			@ 750K.	$150/kw

HP stream		@ 510K	$120/kw	max. available = 6000 kW

LP stream		@ 410K	$ 80/kw	max. available = 4000 kW

Cooling water	300-325K	$ 20/kw

a)	Formulate and solve the LP transshipment that will predict the minimum annual utility cost for HRAT = 10K (without and with constraints on availability of HP and LP steam).

b)	Indicate the loads predicted for the different utilities (in KW) and the location of pinch point(s).

4.  Show that the expanded form of the LP transshipment model can be reduced to the compact LP transshipment model if there are no constraints on the heat loads of the individual matches.

5.  Given the two hot and two cold streams below, determine a selection of matches that feature minimum utility consumption and fewest number of units, and which does not involve a match between hot stream H1 and cold stream C1.  Formulate and solve the corresponding LP and MILP transshipment models.

Stream		Fcp(KW/oC)		Tin(C	)	Tout(C)

H1			1			400		120

H2			2			340		120

C1			1.5			160		400

C2			1.3			100		250

Heating utility at 500oC, Cooling utility at 30oC, HRAT = 20oC

6.	Use the program SYNHEAT to synthesize a heat exchanger network for the following problem:

Fcp(kW/K)		Tin(K)	Tout(K)

H1		      10			650		  370

H2		      20			590		  370

C1		      15			410		  650

C2		     13			350		  500

Heating utility at 680K, cost = $80/kWyr

Cooling utility at 300-320K, cost = $15/kWyr

Individual heat transfer coefficients are 1 kW/m2K.

Cost exchanger = $5000 + 150A

Determine also how the following items change for setting EMAT = 1K, 5 and 15K and draw the corresponding network structures:

a)	Total area

b)	Total investment cost

c)	Total utility cost

d)	Total cost

7	Given is the four component mixture which is to be separated into pure

components;

A	0.15

B	0.3			F = 1000 Kgmol/hr

C	0.35

D	0.2

Assuming sharp splits with high recoveries and identical loads for condenser and reboiler, determine the optimal sequence of distillation columns with an MILP formulation.  Also find the second and third best solutions.

Data

Fixed		Variable	Heat duty coefficients*

System	(103$/yr)	(103$/hr/kgmol yr)	     (106kJ/kgmol)

A/BCD	   145			0.42				0.028

AB/CD	     52			0.12				0.042

ABC/D	     76			0.25				0.054

A/BC		   125			0.78				0.024

AB/C		     44			0.11				0.039

B/CD		     38			0.14				0.040

BC/D		     66			0.21				0.047

A/B		   112			0.39				0.022

B/C		     37			0.08				0.036

C/D		     58			0.19				0.044

*Based on feed flowrate

Cost of utilities:	CW:  $20/kWyr

Steam:  $90/kWyr

8.	Develop a state-equipment network superstructure for the sharp separation of a 	mixture of 4 components (A,B,C,D). Outline the main logic constraints that apply in 	that problem.

9. 	Given are two streams, each of 40 ton/hr, containing two pollutants, A and B. 	Stream 1 contains 100 ppm of A and 20 ppm of B. Stream 2 contains 15 ppm of A 	and 200 ppm of B. It is desired to reduce the concentration of both A and B down 	to 10 ppm each. Assume that there are two treatment units that can be used:

Unit T1 which recovers 5% of A and essentilly all of B, and unit T2 which recovers 2.4% of B and essentially all of A.

a) Develop a superstructure that contains all the alternatives for mixing and splitting the two streams with the two treatment units.

b) Model the problem as an NLP and solve to minimize the sum of total flow going  through the units.

c) Replace the NLP by an LP using the McCormick underestimators for the bilinear terms. Solve the LP and use its solution as starting point for the NLP.

4.	A utility plant must supply the following demands:

a)	Power 1 = 7500 kW

b)	Power 2 = 4500 kW

c)	Medium pressure steam = 25 ton/hr (minimum)

d)	Low pressure steam = 85 ton/hr (minimum)

Develop a superstructure that contains the alternatives described below.

Formulate and solve as an MILP to synthesize a utility system that

requires minimum annual cost.  Also find the second and third best solutions.

Steam:	High pressure 4.83 MPa, 758 K

Medium pressure 2.07 MPa, 523 K

Low pressure 0.34 MPa, 412 K

Steam can be raised with high pressure and/or medium pressure boilers.

Let down valves can be used.

Turbines:

Medium to low are back pressure turbines.

High pressure turbines can be expanded down to medium or to low

pressure, and also have extractions to medium pressure.

Power demands can be satisfied with any of these turbines, but only

one turbine can be assigned to each demand.

Efficiency turbines:     65%

Thermodynamic data:

H (high to medium) = 71 kWhr/ton

H (medium to low) = 112 kWhr/ton

Cost data:

Fixed			Variable

Boiler HP			90,000 $/yr		9,600 $hr/yr ton steam

Boiler MP			40,000 $/yr		8,500 $hr/yr ton steam

MP turbine			25,000 $/yr		14.5 $/kWyr

HP turbine			45,000 $/yr		25 $/kWyr

If extraction is used in HP turbine, an additional fixed charge of 20,000 $/yr  is required.

NOTE:     Do not consider dearator and return of steam condensate.